## Slide 1: SoI Architecture Group
03 Aug 2017

## Slide 2: Agenda
Group Description
Group Objectives
Group Accomplishments
Lessons Learned
Recommended Future Directions

## Slide 3: Group Description
Primary goal: Develop a formal architecture for UxAS in an assume/guarantee framework
Team Members
  Sean Regisford – AFRL
  Aaron Fifarek – LinQuest (LQ)/AFRL
  Brian Hulbert – LinQuest (LQ)/AFRL
  Jen Davis – Rockwell Collins (RC)
  Chris Elliott – Lockheed Martin (LM)
  Ratnesh Kumar – Iowa State University (ISU)
  Cat McGhan – University of Cincinnati (UC)
  Paul Meng – GE
  Hao Ren – Honeywell (H)
  Ben Rodes – Dependable Computing (DC)
  Han Yu – GE

## Slide 4: Group Objectives
Develop a formal architecture for the current state of UxAS in an assume/guarantee framework
Identify strengths, weaknesses, and problems for the current architecture
Document decisions made along the way with supporting rationale
Begin to implement a revised formal architecture to mitigate challenges
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Notes: Current state – did we evolve with UxAS (yes).
Clarify where we used the code (structure) and where we used the Wiki (behavior).
Wanted to formalize UxAS to enable analysis
  Found issues along the way. Fixed some.
  Gave us insights.
To do this, we needed to capture contracts for the components in a formal language.

## Slide 5: Group Accomplishments
UxAS formalization in AADL/AGREE :
  Extracted data types, input and output ports, and connections from code (AFRL/LQ, RC)
  Created formal contracts for nine services and tasks based on the OpenUxAS Wiki and conversations with the developer (DC, RC)
  Stated and analyzed properties of these component-level contracts including timing aspects (DC, RC, LQ)
  Idioms and lemmas developed and documented for effective use of AGREE (DC, RC, LQ/AFRL)
UxAS formalization in ASSERT:
  Created an ontology of the system (GE)
  Examined contractual obligations of a representative component (GE)
Enhanced tool to compose component contracts in AGREE into a system contract (H, ISU)
Created an assurance argument for state machine correctness (DC)
Abstracted a task service finite state machine in Stateflow for simulation and formal analysis (LM)
Connected UxAS to the Robot Operating System (ROS) (UC)
We improved UxAS through formalization
Notes: Restructure?:
Formalized the structure of UxAS as well as behaviors for some tasks and services
Captured and analyzed system properties <- can we say this?
Slide that shows how this work recombines to achieve our goal
*whiteboard this*

## Slide 6: Developing the UxAS Formal Representation

## Slide 7: AADL Tools: Architecture-Driven Assurance
Trusted
Build
Architecture Translation
seL4
eChronos
VxWorks
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
Assurance Case
AGREE
Behavioral Analysis
SIM
Simulation
Kind/JKind
Model Checker
SMT Solvers
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 8: Formalization in AADL/AGREE Formalize Services
Wrote a script to extract data types, input/output ports, and connections from code into AADL
  Abstracted the common message bus by direct port connections
  The structural representation of the Waterways mission is nearly complete
Created formal contracts (captured behaviors) for nine services and tasks based on the OpenUxAS Wiki and conversations with the lead developer
Waterways system level AADL connections diagram
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 9: Formalization in AADL/AGREE UxAS Formal Model Status
Add legible headers for all sections
Services
Tasks
Data Types
Scenarios
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 10: Formalization in AADL/AGREE UxAS Formal Model Status
Add legible headers for all sections
Services
Tasks
Data Types
Logging and Data Services
Scenarios
Communication Services
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 11: Formalization in AADL/AGREE What Did We Prove?
Realizability
  Checks that a component implementation is possible and that there are no conflicts amongst the guarantees in the component’s contract
Assume/guarantee reasoning
  Checks higher-level guarantees and lemmas using the guarantees of the subcomponents, and checks that the assumptions of the subcomponents hold
    Check that all input/output events are possible
    Capture response times in components and analyze system-level response times
    Analyze behavior of state machines that represent component behavior
Some analysis results for the Route Aggregator Service
(Aggregator Role):
Rockwell Collins, Dependable Computing, AFRL/LinQuest
Observers
Notes: Consider adding or replacing with a screenshot of a Waterways timing guarantee
Use term observer and explain it.
Maybe add another slide with actual contracts.

## Slide 12: Formalization in AADL/AGREE What Did We Learn?
Idioms and lemmas developed and documented for effective use of AGREE
  “Eventual” behavior on state transitions
  Tracking and maintaining IDs
  Dummy parent components for proving lemmas
  Preventing inadvertent solutions space constraints
  Abstraction of complex data structures
  Skolemization idea for arrays
  Fully specifying output event conditions
  Use of AGREE connections
  Real-time patterns
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 13: System-level contracts
System-level guarantees are in progress
  Responsiveness/timing example
  Task Manager Service:
  Waterways (system-level) – not yet proven:
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 14: System-level contracts
System-level guarantees are in progress
Challenges
  Many system-level requirements for UxAS are informal
  Others require significant infrastructure (supporting contract guarantees) in order to prove them
Perhaps we can compose the component contracts we have to discover new system-level properties…
Rockwell Collins, Dependable Computing, AFRL/LinQuest

## Slide 15: Quantifier Elimination based Property Composition and Verification
Strongest system property: the system property that implies any other system properties established upon the given constraints of component properties and their connectivity.
Quantifier Elimination: a powerful technique for gaining insight, through simplification, into problems involving
logic expressions in various theories.
Component variables: System variables: Component contracts: Connectivity set:
Theorem: The strongest system property, established upon the component contracts and connectivity is given by:
Prove postulated system property from the strongest system property:
Honeywell, Iowa State University
Notes: Maybe bridge here with system-level timing properties and their difficulty
Formula is for non-time-dependent systems
Can reuse strongest system property to prove other postulated properties. Can save analysis time.
Can be reduced to QE problem

## Slide 16: Quantifier Elimination based Property Composition and Verification
Strongest system property: the system property that implies any other system properties established upon the given constraints of component properties and their connectivity.
Quantifier Elimination: a powerful technique for gaining insight, through simplification, into problems involving
logic expressions in various theories.
Component variables: System variables: Component contracts: Connectivity set:
Theorem: The strongest system property, established upon the component contracts and connectivity is given by:
Prove postulated system property from the strongest system property:
AGREE contracts can be composed into a system-level contract
Honeywell, Iowa State University

## Slide 17: Implementation and Experimental Result
Eclipse
AGREE
OSATE2
Extended-AGREE
Redlog
result
.aadl
Redlog-integrated AGREE:
Redlog model
Result parser
Honeywell, Iowa State University
Notes: * Redlog is the QE solver (substitute for Jkind).

## Slide 18: Formalization in ASSERT Proposed Approach
Software Codebase
(C, C++, Java, C#, Python, Ada, …)
Reverse Engineering
Software Design Information
Architecture Information Extraction
Automated Ontology Generation
Architecture & Ontology Mapping Template
Ontology Model
ASSERT™ SADL Ontology files
(.sadl files)
*SADL: Semantic Application Design Language
Extract architecture information through reverse engineering.
Transform extracted architecture information into SADL ontology.
Import SADL ontology into ASSERT™ to enable requirement capture, analysis, and test generation in ASSERT™
GE
Notes: Grab Tony’s version(?)
Two parts:
Import C++ to Enterprise Architect (“reverse engineering button”)
Use API to extract ontology (interfaces and connections)
Implement XML parser for message types -> output SADL for message type definition

## Slide 19: Modeling UxAS System Architecture in SADL Ontology
GE
Notes: *Subtypes capture the inheritance hierarchy

## Slide 20: Modeling Message Type Definition in SADL Ontology
GE

## Slide 21: Modeling Dataflow in SADL Ontology
Context:
TaskAssignmentSummary__Subscription of PlanBuilderService is TaskAssignmentSummary_out of AssignmentTreeBranchBoundBase
and
TaskImplementationRequest__Subscription of TaskServiceBase is TaskImplementationRequest_out of PlanBuilderService
and
…
Illustrative Example in SADL Ontology
PlanBuilder
Service
AssignmentTreeBranchBoundBase
TaskServiceBase
TaskImplementationRequest_out
TaskImplementationRequest_Subscription
TaskAssignmentSummary_out
TaskAssignmentSummary_Subscription
GE

## Slide 22: Illustrative example: Sample AADL Contracts Captured in SADL
GE

## Slide 23: Illustrative example: Contracts Analysis
Conflicts!
A counter example:
num_route_requests_being_serviced = 1561
routePlanRequest_In of RouteAggregatorService is received
previous state of RouteAggregatorService is IDLE
state of RouteAggregatorService could be either PENDING or IDLE!
GE

## Slide 24: Formalization in ASSERT Illustrative example: Modified Contracts Pass Analysis
What we learned: errors introduced in the manual contracts/requirements capturing process can be found earlier through automated analysis.
GE
Analysis enabled:
Redundancy check
Conflict check
Completeness check (e.g., handle all cases of a variable’s value)

## Slide 25: From the lead developer: Impact of Formalization on UxAS
Recognition of key assumptions
  IDs are unique (not guaranteed by the implementation today)
Illumination of design flaws
  Missing ID checks
  All services need to use the Route Planner for routes to ensure there is no conflict with an airspace constraint
Restructuring to avoid redundant or problematic logic
  Split RouteAggregatorService into two services for two functional roles
  Removal of some dead code in the Route Planner
We improved UxAS through formalization
Notes: *Victory slide*
Note that this came from Derek

## Slide 26: State Machine Reasoning

## Slide 27: State Machine for the Route Aggregator Service
IDLE
PENDING

## Slide 28: State Machine Reasoning in AGREE
Example properties that we can prove:
  States are reachable
  Transitions are viable
Even so, the (human) modeler can make mistakes
We use an assurance case to capture the rest of the argument

## Slide 29: State Machine Correctness Argument
Argument pattern for individual AADL component state machine correctness:
  Structure repeated for each component
  Vision: Situated within a larger model correctness argument
Argument situates proposed AGREE lemmas:
  Purpose
  Rationale
  Limitations and benefits
Dependable Computing

## Slide 30: Argument-Derived Observations
Best practices/standards for AADL/AGREE use are needed
  Situate proofs within modeling fault analysis/mitigation
  Supports arguments that the set of lemmas are complete and correct
Additional tool support to reduce human error
  E.g., lemmas and repetitive infrastructure are developed manually
  Minimize repetitive concerns in the argument about human error
Enhanced integration between AADL and AGREE
  Minimize repetitive arguments about AADL and AGREE consistency/agreement
A simpler higher-level protocol state machine spec for validation
  Provide a structure to validate against
  Simplify validation activity and simplify validation arguments
Dependable Computing

## Slide 31: Stateflow Representation
Benefits
  Enable simulation
  Enable analysis from Simulink
    QVtrace
    Simulink-to-PVS
    Simulink Design Verifier
  Visualize counterexamples
  Evidence in the assurance argument: “gold standard state machine”
Created a Stateflow representation of the Task Service Base state machine
Simulink/Stateflow abstractions cross-checked with AADL model
  Found erroneous initial conditions, unused from/goto flags, and incorrect settings on if-else cases in Stateflow model
Lockheed Martin, Dependable Computing, Rockwell Collins

## Slide 32
Notes: Each state has a sub state machine. Emulates failure in each state.

## Slide 33
Analysis with QVtrace
Matlab Simulink Construction for Simulation  QVtrace
QVtrace is a model checker for Simulink that uses SMT Solvers such as Z3
Helped validate expected behavior of the abstraction
Lockheed Martin, Dependable Computing, Rockwell Collins
Enables path from contracts to code generation

## Slide 34: Lessons Learned
Many problems are identified through the process of formalization, before analysis
Data types (or an ontology), ports, and connections can be automatically extracted from code (with some moderate up front work)
Reusable (template) properties help find common mistakes
Not every error can be detected with a template property--a review of the specification itself is still worthwhile
Assurance arguments are useful to capture the “rest of the story”
SpeAR, ASSERT, AADL/AGREE, and QVtrace are all very capable analysis tools. There are synergies between them.
Challenges: arrays, inheritance
Notes: Assurance arguments:
  Differences between the model and the real world
  Specification versus intent
  Enhancements to the formal analysis tools could simplify the argument

## Slide 35: Recommended Future Directions
Write contracts for the remaining thirty-one components
State/compose and analyze system-level properties (in progress)
Generate code from AADL
Generate test cases from AGREE and run on UxAS implementation
Continue documenting decisions and the assurance case for the architecture
Notes: Discuss: Model of Heterogeneous System (Distributed Mission-Task-Autopilot Management-Dubin)

## Slide 36: Backup
Notes: Maybe show a contract for a service
22 min at dry run

## Slide 37: Formalization in ASSERT SADL Ontology Generation
Modeling Message Type Definition
Architecture Group
  Context:
  TaskAssignmentSummary__Subscription of PlanBuilderService is TaskAssignmentSummary_out of AssignmentTreeBranchBoundBase
  and
  TaskImplementationRequest__Subscription of TaskServiceBase is TaskImplementationRequest_out of PlanBuilderService
  and
  …
PlanBuilderService
AssignmentTreeBranchBoundBase
TaskServiceBase
TaskImplementationRequest_out
TaskImplementationRequest_Subscription
TaskAssignmentSummary_out
TaskAssignmentSummary_Subscription
Modeling Dataflow in SADL Ontology
GE
Notes: Improve legibility (maybe go back to two slides)

## Slide 38: Producing the Formal Architecture
The formal architecture relied on the documentation that was found on the UxAS Wiki page.
  Direct code decomposition was going to be too intensive to meet objectives efficiently.
  Through formalization, gaps were identified.
Just the effort to formalize components proved extremely valuable to the SMEs, even before the analysis.